## Slide 1: Camera Self-Calibration in UAV Photogrammetry: When is it Viable?
Prof. Clive Fraser
Dept. of Infrastructure Engineering University of Melbourne, Australia
ASPRS Annual Conference and International Lidar Mapping Forum, Denver, January 27-31, 2019

## Slide 2
Cameras for Drones/UAS/UAVs
Vary from off-the-shelf point & shoot, to zoom compact, mirrorless, super-zoom, DSLRs and numerous specially designed cameras
Universal requirement for photogrammetric applications: cameras must be calibrated

## Slide 3
UAVs for Spatial Information Generation
Networks can be regular or irregular
Photogrammetric processing must accommodate every configuration

## Slide 4
Sensor Calibration, Orientation & 3D Object reconstruction
Bundle Adjustment with Self-Calibration
(A)
Manual to Semi-Automated Image Measurement
(B)
Automatic, using coded targets
(C)
Automatic with no targets (SfM approach)
Initial Network Relative Orientation
Bundle adjustment (+self-calibration) for Refined Network Relative/Exterior Orientation
(B)
Automatic 3D coordinates for targetted points
(C)
Automatic generation of dense point cloud – no targets
(SfM or FBM approach)
Subsequent Determination of 3D Points (generally with final Bundle Adjustment)
(A)
Manual or semi-automated referencing or measurement of targetted or untargetted points
UAVs/Drones

## Slide 5: Network Geometry for Self-Calibration
Multi-image, convergent network
Orthogonal camera roll angles
Depth in the object space (not mandatory, but very desirable)
Highly redundant network (all pts >6 ray)
High image measurement accuracy (targets: sxy to 0.03 pixel for monochrome CCD & generally 0.1 pixel for colour; targetless: sxy to 0.3 pixel for FBM/SfM)
Plus
Unifocal lens (desirable), fixed focus
Stable interior orientation
Attributes of successful self-calibration networks, when there is no ground or camera station positional control:

## Slide 6: FBM/SfM-Based Orientation with Free-Network Self-Calibration
SfM-based approach affords massive redundancy to compensate for potential modest loss in geometric strength
Salzspeicher network: 23 images, 46,000 points, RMS vxy = 0.25 pixel

## Slide 7: On-Ground Calibration via Free-Network Self-Calibration
A very feasible approach for short focal length UAS cameras
Results of 6 separate self-calibrations of a 20mpixel Phantom P4P camera
Note high level of calibration stability of the Phantom 4 PRO camera

## Slide 8
Unordered UAV Networks for Free-Network Self-Calibration
UAV image block, 344 images & 9700 points, all pts in >4 images; most in >20.
Limited convergence, limited depth in obj. space, RMS vxy=0.4pl
Strong self-calibration achieved
176-ray point

## Slide 9
‘Standard’ UAV Network, OK for Free-Net Self-Calibration?
‘Regular’ block of 297 images & 480,000 points, 68K pts in >6 images; many in >10.
No convergence, no orthogonal roll, limited depth in obj. space, RMS vxy=0.8pl
No!
Self-calibration of IO not feasible; lens distortion possibly OK, depending upon overlap
Essential Requirement :
Maximise Scale Variation both within & between Images
In order to
Minimize Projective Coupling between Calibration & Exterior Orientation Parameters:

## Slide 10
Self-Calibration very Problematic in a ‘Standard’ UAV Network Requires both GCPs & Camera Stn Positional Constraints
Regular block of 203 images & 183,000 points, 95K pts in >6 images; 3K in >20.
No convergence, no orthogonal roll, limited depth in obj. space, RMS vxy=0.36pl
Control to support camera self-calibration comprised both GCPs & Camera Stn GPS posn’s
Note: usually one of two aims being pursued through self-calibration:
i) provide systematic error compensation, not necessarily camera calibration per se
ii) to provide a scene-independent calibration of the camera(s)

## Slide 11
Case 1: ‘Standard’ aerial block with large depth variation in object space
Geometric Attributes of UAV Networks for Self-Calibration
Oriented UAV image block of 127 images & 180,000 points, 31K pts in >6 images; many in >10.
No convergence, no orthogonal roll, but very significant depth in obj. space (H-h varies from 130m to 290m, so scale varies within some images by 50% from the mean), RMS vxy=0.45pl
Full self-calibration of IO & lens distortion feasible, good precision & low projective couplings
(no need for object space control)
18 million points in cloud

## Slide 12
Case 2: Mixed range network (scale variation between images, not within)
Geometric Attributes of UAV Networks for Self-Calibration
UAV image block of 84 images & 30,000 pts in >6 images; many in >10.
No convergence, no roll, but significant scale diff. between 3 flying heights, RMS vxy=0.8pl
Full self-calibration of IO & lens distortion feasible, but strong projective coupling between principal distance & camera stn Z coord. (ideal example of where in-air & on-ground GPS constraints should apply)
H = 10m
H = 30m
H = 20m

## Slide 13
Case 3: Highly overlapping oblique imagery of a 3D object scene (images from FMV)
Geometric Attributes of UAV Networks for Self-Calibration
UAV image block of 56 images & 28K points, 200 with >6 rays, RMS vxy=0.44pl
No convergence, no roll, but significant scale diff. within each image, and 3D
Full self-calibration of IO & lens distortion feasible, moderate precision with moderate projective couplings (espec. related to IO/EO and decentring distortion)
(no requirement for object space control)

## Slide 14
Case 3: Highly overlapping oblique imagery of a 3D object scene (images from FMV)
Geometric Attributes of UAV Networks for Self-Calibration
UAV image block of 56 images & 28K points, 200 with >6 rays, RMS vxy=0.44pl
No convergence, no roll, but significant scale diff. within each image, and 3D
Full self-calibration of IO & lens distortion feasible, moderate precision with moderate projective couplings (espec. related to IO/EO and decentring distortion)
(no requirement for object space control)

## Slide 15
Case 4: Network for 3D reconstruction of a historic barn
Geometric Attributes of UAV Networks for Self-Calibration
UAV image network of 49 images & 50K points, 6000 with >6 rays, RMS vxy=0.3pl
No convergence, no roll, but significant scale diff. within each image
Full self-calibration of IO & lens distortion feasible, moderate precision with moderate projective couplings (no necessity for object space control)

## Slide 16
Case 4: Network for 3D reconstruction of a historic barn
Geometric Attributes of UAV Networks for Self-Calibration
Self-calibration OK due to substantial variation in image scale within each image, but note projective linkage between principal point & elevation angle/Z
Recovery of IO is moderately strong (sigmas of a few micrometers)

## Slide 17
Case 5: 2-camera ISPRS benchmark network
Geometric Attributes of UAV Networks for Self-Calibration
UAV image block of 224 images & >150K points, RMS vxy=0.4pl
‘Accidental’ convergence, no roll & limited scale variation within the images
Full self-calibration feasible but not strong, high projective coupling espec. between IO & EO
(Camera roll would dramatically improve accurate IO recovery)

## Slide 18
Case 6: P4P Block with additional convergent images
Geometric Attributes of UAV Networks for Self-Calibration
UAV image block of 266 images (203 nadir & 66 convergent) & 270K points, RMS vxy=0.39pl
Many points meas. in >50 images)
Supports strong self-calibration

## Slide 19: In-air versus on-ground calibration via self-calibration of P4P
Recall importance of image scale variation
Obj XYZ discrepancies: <1mm in XY, 3mm in Z for tgts, 5mm for SfM

## Slide 20: Affine distortion in object space – a problem?
Differential scale difference between XY and Z
length of vectors at ground level is 6 – 9mm

## Slide 21: Not just an IO issue! Self-calibration of radial distortion only is also not recommended in blocks of imagery with moderate overlap!
Should not constrain GPS cam. stn coords since accuracy too low (0.5m RMS)
Result: classical doming of terrain, Z-discrepancy range of -0.9m to +0.51m
Flying Ht= 35m
53 images
32,000 pts
RMSvxy = 0.51 pl
sXY= 4mm
sZ= 10mm
1m

## Slide 22: Constraints in Bundle Adjustment of UAV Image Blocks
Precision  Weights
Image coord. obs. sxy  P
GCPs sXYZ  P2
GPS camera stns. sXcYcZc  P1
PURPOSE: To remove both datum & configuration defects
Bundle Adjustment Normal Equations

## Slide 23: Relative Magnitude of Constraints
Image coord. obs. sxy  P
GCPs sXYZ  P2
GPS camera stns. sXcYcZc  P1
Example: If H=60m, f = 8.8mm, pixel size = 2.4 mm & sxy = 0.4 pixel,
then sxy* = (60m/8.8mm) * (0.4*2.4mm) ≈ 7mm
Consider the case: sxy* ≈ sXYZ ≈ sXcYcZc
Where: sxy* = Scale No. * sxy
Consider the number of constraints in FBM/SfM Bundle Adjustment
sxy* sXYZ sXcYcZc
10,000s - 100,000s 10s 100s -1000s
The relative magnitudes of sXYZ & sXcYcZc against sxy* are critically important in self-calibration within UAV image networks

## Slide 24: GCP & Cam. Stn. Constraints in UAV Image Blocks
The a priori weighting (ie standard errors) assigned to GCPs and Camera Station GPS observations is very important for camera self-calibration
Two options for removal of the configuration defect to support self-calibration:
Utilise a network geometry that supports constraint-free self-calibration (especially of c, xp, yp)
And/or
Impose object-space constraints sXYZ & sXcYcZc << sxy* such that projective coupling of IO & EO parameters is sufficiently suppressed, and imposed ‘control’ leads to a BA normal equation matrix of full rank

## Slide 25
Example of Impact of Weighting on Perturbed GCPs
DZ errors resulting from BA with different assigned weights
UAV Network has 59 images & 21,000 object points, GSD = 0.016m
Sigmas of Camera Station GPS data set at 0.02m (residuals at 0.05 - 0.1m level)
Mean std error from Free-Network BA: sXY = 0.006m, sZ = 0.022m
Total of 10 GCPs/checkpoints (shown; 3 featured in following table)
Took ‘near perfect’ solution & perturbed the Z-coordinate of each GCP from 5 to 10 times sZ , ie from 0.10m to 0.20m
Wanted to assess impact of GCP weights on the recovery of Z perturbations

## Slide 26
GCP Std. Errors (sGCP) (m) | RMS vxy (pixel) | DZ GCP 1 Intro. Error DZ=-0.15 | DZ GCP 2 Intro. Error DZ=+0.20 | DZ GCP 3 Intro. Error DZ=-0.20 | All points RMSE XY | All points RMSE Z
0.01 | 0.33 | -0.02 | 0.01 | -0.01 | 0.001 | 0.003
0.005 | 0.33 | -0.02 | 0.01 | -0.01 | 0.001 | 0.003
0.001 | 0.33 | -0.12 | 0.12 | -0.16 | 0.002 | 0.004
0.0001 | 0.33 | -0.15 | 0.18 | -0.22 | 0.002 | 0.006
Example of Impact of Weighting on Perturbed GCPs
DZ errors resulting from BA with diff. weights
GCPs have no practical impact upon BA until assigned sGCPs << sxy*
(ie weighted constraints must be very tight to enforce fit to control!)
Especially important consideration if self-calibration is to be applied

## Slide 27: Example Multi-level UAV Network Geometry suited to Self-Calibration in the Absence of GCPs
20,000 – 80,000 FBM points
10 GCPs to ‘few cm’ accuracy
H-h = 30m
52 nadir images
H-h = 40m
68 convergent images
H-h = 68m (GSD = 16mm)
59 nadir images
H-h = 105m
66 nadir images
UAV camera: Sony A6000

## Slide 28: Number of Viable Self-Calibration Configurations
H-h = 105m
Convergent imaging
3-level nadir
Nadir + convergent

## Slide 29: Self-Calibration Results for A600 from 5 Networks

## Slide 30: Consider Self-Calibration from Single Ht Mission via CONTROL
GCPs
59 images, 21,000 points,
GSD = 0.016m, sxy* = 0.006m
Camera Station GPS (sXcYcZc = 0.02m)
10 GCPs
Many pts in >30 images

## Slide 31: Network bias & shape distortion with varying sGCP values (1)
GCPs
sGCP =0.0001 | X (m) | Y (m) | Z (m)
Posn. Bias | 0 | 0 | 0
RMS Posn. Discrepancy | 0.003 | 0.003 | 0.013
sGCP = 0.001 | X (m) | Y (m) | Z (m)
Posn. Bias | 0 | -0.001 | -0.002
RMS Posn. Discrepancy | 0.003 | 0.003 | 0.010
sGCP = 0.005 | X (m) | Y (m) | Z (m)
Posn. Bias | 0.002 | -0.008 | -0.003
RMS Posn. Discrepancy | 0.004 | 0.009 | 0.016
Design Accuracy: sXY = 0.006, sZ =0.023

## Slide 32: Network bias & shape distortion with varying sGCP values (2)
GCPs
sGCP =0.01 | X (m) | Y (m) | Z (m)
Posn. Bias | -0.002 | -0.015 | 0.014
RMS Posn. Discrepancy | 0.008 | 0.018 | 0.026
sGCP = 0.025 | X (m) | Y (m) | Z (m)
Posn. Bias | 0 | -0.017 | 0.072
RMS Posn. Discrepancy | 0.025 | 0.036 | 0.078
sGCP = 0.05 | X (m) | Y (m) | Z (m)
Posn. Bias | 0.004 | -0.019 | 0.157
RMS Posn. Discrepancy | 0.049 | 0.067 | 0.162
Design Accuracy: sXY = 0.006, sZ =0.023

## Slide 33
The network geometry rules regarding self-calibration apply to UAV/UAS networks – there are no shortcuts!
Consider comprehensive pre-calibration & assessment of calibration stability; multi-scale networks preferred over constrained single-scale
Not only IO calibration is problematic for near-nadir UAS networks w/o EO constraints; self-calibration of radial distortion also a problem
GPS camera stn. constraints in self-calibration are generally useful in UAS networks only when GPS accuracy is cm level – not yet the norm
Biases & distortions in point positioning are not necessarily removed through the use of moderately to tightly constrained GCPs
Covariance matrices only realistic when datum & configuration defects removed – helped by control sXYZ & sXcYcZc << sxy*
Object point biases & distortions can be >> magnitude indicated by object point XYZ sigmas
Concluding Remarks

## Slide 34
Concluding Remark
To ensure successful self-calibration: Maximise image scale variation within and between images forming the network … and utilise roll angle variation
Thank You