## Slide 1: Implementation of GNSS/INS-assisted Structure from Motion for a Thermal Camera onboard Unmanned Aerial System
Meghdad Hasheminasab, Tian Zhou, Lisa Laforest, Evan Flatt, and Ayman Habib
Digital Photogrammetry Research Group
Lyles School of Civil Engineering
Purdue University
Webpage: http://purdue.edu/CE/DPRG

## Slide 2: Introduction
Thermal imaging sensors and their applications
Precision agriculture: Plant disease detection, estimating crop yield, improving land cover classification, etc.
To achieve these goals, generating precise orthophotos is a key step.
What are the challenges towards orthophoto generation from thermal images?
Crash scene reconstruction
Precision agriculture
Public safety [1]
high
low
[1]:Leykin, A., & Hammoud, R. (2006, June). Robust multi-pedestrian tracking in thermal- visible surveillance videos. In Computer Vision and Pattern Recognition Workshop, 2006. CVPRW'06. Conference on (pp. 136-136). IEEE.
Notes: Thermal imaging systems usually detect radiation in the long-infrared range of the electromagnetic spectrum (9-14 um) and produce image of that radiation.

## Slide 3: Aerial Triangulations: Conventional Framework
Several commercial packages for AT:
Conventional Structure from Motion (SfM) strategy:
Pix4D
PhotoScan
DronDeploy
…
Image Matching
Automated Relative Orientation
+
Mismatch Removal
Exterior Orientation Recovery
Global Bundle Adjustment with System Calibration
+
Georeferencing Control
SIFT
SURF
…
RANSAC
Epipolar Geometry
…
8-point
8-point normalized
5-point (Nister)
…
Incremental Strategy
Global Strategy
Final Products:
DSM,
Orthophoto
Calibration Parameters
…
Input Image Dataset
Provide precise products when using RGB images
IOPs, EOPs, DSM
Aerial Triangulation
Orthophoto

## Slide 4: Aerial Triangulation: RGB vs. Thermal
Image matching: RGB images vs. thermal images
Can we separate “Matching” & “ROPs Estimation” steps?
Poor Matching
(wrong & insufficient matches)
Poor Relative Orientation
Poor 3D Reconstruction

## Slide 5: GNSS/INS-assisted SfM
Estimation of Relative Orientation Parameters using GNSS/INS information
Key factors: mounting parameters, system synchronization
Calibration information
GNSS/INS Information
EOPs information
ROPs information (unknown)
Time
Time

## Slide 6: GNSS/INS-assisted SfM: Workflow
Relative Orientation Recovery
Mismatch Removal
Exterior Orientation Recovery
Global Bundle Adjustment with System Calibration
+
GNSS/INS Data
GNSS/INS Data
+
System Calibration
Prior Knowledge about Object Space
SIFT
PC2
Ground point
Right Image point
Left Image point
Incremental Strategy
PC1
DSM generated from the prior knowledge regarding the object space
Input Image Dataset
Image Matching

×
×
Final Products:
DSM,
Orthophoto
Calibration Parameters
…
Workflow
Mismatch Removal

## Slide 7: DJI M200 Platform
 | Nominal Lever Arm and Boresight Angles between thermal camera and GNSS/INS body frame |  |  |  |  |  | Sensor’s intrinsic parameters |  |  | 
Sensor | Δω (degree) | Δφ (degree) | Δκ (degree) | Δx (m) | Δy (m) | Δz (m) | Array size | Focal length (pixel) | Pixel size (um) | Distortion parameters
Thermal | 180 | 0 | -90 | 0.045 | -0.015 | 0.045 | 640 512 | 1117.64 | 17 | N/A
RGB | 180 | 0 | -90 | 0.045 | 0.025 | 0.050 | 4000 3000 | 4324.30 | 1.85 | N/A
 | Nominal Lever Arm and Boresight Angles between thermal camera and GNSS/INS body frame |  |  |  |  |  | Sensor’s intrinsic parameters |  |  | 
Sensor | Δω (degree) | Δφ (degree) | Δκ (degree) | Δx (m) | Δy (m) | Δz (m) | Array size | Focal length (pixel) | Pixel size (um) | Distortion parameters
Thermal | 180 | 0 | -90 | 0.045 | -0.015 | 0.045 |  | 1117.64 | 17 | N/A
RGB | 180 | 0 | -90 | 0.045 | 0.025 | 0.050 |  | 4324.30 | 1.85 | N/A
Body Frame
Flying Direction
Camera Frame
RGB sensor
Thermal sensor
FLIR Duo Pro R
manual measurements and system setups
provided by the manufacturer

## Slide 8: Flight Parameters & Area of Study
Date | Field | Flying Height | Flying Speed | GSD Thermal | GSD RGB | Overlap Thermal_RGB | Side-lap Thermal_RGB | Number of Flight Lines | Number of Images
20180725 | 9D ACRE | 20 m | 2.7 m/s | 1.8 cm | 0.5 cm | 70%_80% | 70%_80% | 6 | 284
 |  | 40 m | 5.4 m/s | 3.6 cm | 1 cm |  |  | 6 | 164
20180914 | 9D ACRE | 20 m | 2.7 m/s | 1.8 cm | 0.5 cm | 70%_80% | 70%_80% | 6 | 294
 |  | 40 m | 5.4 m/s | 3.6 cm | 1 cm |  |  | 6 | 168
Ground Targets
40m flight trajectory
20m flight trajectory

## Slide 9: Hypotheses
RGB and Thermal cameras capture images simultaneously.
GNSS/INS event marker coincides with the exposure time for both cameras.

## Slide 10: Problem Statement & Proposed Solution
Problems:
  By analyzing the generated orthophoto, a time delay between when the images are captured and when the event marker is recorded was discovered.
  RGB & Thermal camera images are not captured at the same time.
  Time delay leads to inaccurate calibration parameters and poor orthophotos and reconstruction of object space.
Proposed Solution:
  Solve for the time delay as an unknown in bundle adjustment process.

## Slide 11: Collinearity Equations
Object point I
2. GNSS/INS
body frame
1. Mapping Frame
3. Image sensor
PC
Image point
Question:
What parameters will be affected by existence of a time delay in the system?
Collinearity equations while considering GNSS/INS information:

## Slide 12: Modified Collinearity Equations,
Flight Trajectory

## Slide 13: Modified Collinearity Equations,
Collinearity Equations:
Trajectory
How can we estimate ?
Angular
Velocity
Modified Collinearity Equations:

## Slide 14: Calibration Results: Thermal Camera
Ground targets are considers as tie points.
Estimated system parameters: boresight angles, lever arm
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) | Estimated boresight Δ | Estimated boresight | Estimated boresight Δ
July 25th | N/A | 0.032 | -0.146 | 178.46 | 1.22 | -90.78
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) |  |  | 
July 25th | N/A | 0.032 | -0.146 | 178.46 | 1.22 | -90.78
Statistics on five check points on orthophoto for FLIR-Thermal sensor* |  |  | 
 | Mean-X/Y (m) | Standard Deviation- X/Y(m) | RMSE- X/Y (m)
July 25th | N/A | N/A | N/A
* Check targets could not be identified in the generated orthophoto.

## Slide 15: Results: Without Considering Time Delay
July 25th Thermal Dataset
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm | SfM-based
Generated orthophoto with 1cm resolution
GSD 0.03 m
* Check targets could not be identified in the generated orthophoto.

## Slide 16: Calibration Results: Thermal Camera
Ground targets are considers as tie points.
Estimated system parameters: boresight angles, lever arm, time delay
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) | Estimated boresight Δ | Estimated boresight | Estimated boresight Δ
July 25th | -267 | 0.115 | -0.033 | 178.54 | -0.53 | -90.82
Sept 14th | -260 | 0.094 | -0.032 | 178.51 | -0.66 | -90.50
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) |  |  | 
July 25th | -267 | 0.115 | -0.033 | 178.54 | -0.53 | -90.82
Sept 14th | -260 | 0.094 | -0.032 | 178.51 | -0.66 | -90.50
Statistics on five check points on orthophoto for FLIR-thermal sensor |  |  | 
 | Mean-X/Y (m) | Standard Deviation- X/Y (m) | RMSE- X/Y (m)
July 25th | -0.03/ -0.07 | ±0.08/ 0.02 | 0.08/ 0.08
Sept 14th | -0.05/ -0.03 | ±0.06/ 0.02 | 0.06/ 0.04

## Slide 17: Results: July 25th Thermal Dataset
GSD 0.03 m
Red boxes show the targets
Generated orthophoto with 1cm resolution
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based
Trajectory | System Parameters | DSM
SfM-based | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based

## Slide 18: Results: September 14th Thermal Dataset
GSD 0.03 m
Red boxes show the targets
Generated orthophoto with 1cm resolution
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based
Trajectory | System Parameters | DSM
SfM-based | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based

## Slide 19: Calibration Results: RGB Camera
Ground targets are considers as tie points.
Estimated system parameters: boresight angles, lever arm
Calibration Results for FLIR-RGB Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) | Estimated boresight Δ | Estimated boresight | Estimated boresight Δ
July 25th | N/A | 0.12 | -0.06 | 178.43 | 1.65 | -91.08
Calibration Results for FLIR-RGB Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) |  |  | 
July 25th | N/A | 0.12 | -0.06 | 178.43 | 1.65 | -91.08
Statistics on five check points on orthophoto for FLIR-RGB sensor* |  |  | 
 | Mean-X/Y (m) | Standard Deviation- X/Y (m) | RMSE- X/Y (m)
July 25th | N/A | N/A | N/A
* Check targets could not be identified in the generated orthophoto.

## Slide 20: Results: Without Considering Time Delay
July 25th RGB Dataset
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm | SfM-based
Generated orthophoto with 1cm resolution
GSD 0.01 m
* Check targets could not be identified in the generated orthophoto.

## Slide 21: Calibration Results: RGB Camera
Ground targets are considers as tie points.
Estimated system parameters: boresight angles, lever arm, time delay
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) | Estimated boresight Δ | Estimated boresight | Estimated boresight Δ
July 25th | -205 | 0.068 | 0.005 | 178.47 | 0.06 | -90.92
Sept 14th | -203 | 0.072 | 0.009 | 178.48 | 0.11 | -90.84
Calibration Results for FLIR-Thermal Sensor |  |  |  |  |  | 
 | Estimated time delay Δt (ms) | Estimated lever arm ΔX (m) | Estimated lever arm ΔY (m) |  |  | 
July 25th | -205 | 0.068 | 0.005 | 178.47 | 0.06 | -90.92
Sept 14th | -203 | 0.072 | 0.009 | 178.48 | 0.11 | -90.84
Statistics on five check points on orthophoto for FLIR-thermal sensor |  |  | 
 | Mean-X/Y (m) | Standard Deviation- X/Y(m) | RMSE- X/Y (m)
July 25th | -0.04/ -0.06 | ±0.04/ 0.02 | 0.05/ 0.06
Sept 14th | -0.01/ 0.02 | ±0.02/ 0.03 | 0.03/ 0.03

## Slide 22: Results: July 25th RGB Dataset
GSD 0.01 m
Red boxes show the targets
Generated orthophoto with 1cm resolution
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based
Trajectory | System Parameters | DSM
SfM-based | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based

## Slide 23: Results: September 14th RGB Dataset
GSD 0.01 m
Red boxes show the targets
Generated orthophoto with 1cm resolution
Trajectory | System Parameters | DSM
Original | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based
Trajectory | System Parameters | DSM
SfM-based | Estimated Boresight Angles Estimated Lever Arm Estimated Time Delay | SfM-based

## Slide 24: Conclusions & Future Work
GNSS/INS-assisted SfM has been shown as a simple and robust approach for 3D reconstruction of thermal imagery.
With consumer-grade systems, a time delay between the GNSS/INS and the actual exposure time may exist.
The proposed time delay estimation approach leads to accurate 3D reconstruction and 2D orthophotos.
Based on the results, we can conclude that the time delay for the used sensor is consistent throughout the time but is different for Thermal and RGB sensors
Time delay estimation in Multi-Camera systems for indoor mapping applications is the focus of current and future work.

## Slide 25
Thank you!
The information, data, or work presented herein was funded in part by the Advanced Research Projects Agency-Energy (ARPA-E), U.S. Department of Energy, under Award Number DE-AR0000593. The views and opinions of authors expressed herein do not necessarily state or reflect those of the U.S. Government or any agency thereof.
Acknowledgement