## Slide 1: Digital Imagery Spatial Resolution and Radiometry: Metrics and Assessments
Mary Pagnutti
Kara Holekamp
Robert E. Ryan
Innovative Imaging and Research
Building 1103 Suite 140 C
Stennis Space Center, MS 39529
ASPRS 2012 Annual Conference
Sacramento, California
March 22, 2012

## Slide 2: Introduction
Mapping and remote sensing systems are becoming indistinguishable
High spatial resolution satellites are designed and specified to do both

## Slide 3: Introduction (Continued)
Aerial and satellite digital imaging systems are very similar with the following exceptions
  Differ in the amount of atmosphere and collection geometries
  Typically not as extensively characterized
    Radiometry and spatial resolution specifications not emphasized
    Spatial resolutions depends on altitude (satellites altitudes are typically fixed)
    Both radiometry and spatial resolution are not simple to validate (Part of the reason limited specification)

## Slide 4: Introduction (Continued)
Aerial and satellite digital imaging systems are very similar with the following exceptions
  Differ in the amount of atmosphere and collection geometries
  Typically not as extensively characterized
    Radiometry and spatial resolution specifications not emphasized
    Spatial resolutions depends on altitude (satellites altitudes are fixed)
    Both are not the simple to validate (Part of the reason limited specification)

## Slide 5: Spatial Resolution

## Slide 6: Spatial Resolution
Depends on:
  Pixel size, measured by:
    Ground Sample Distance (GSD)
  Point Spread Function (PSF) - the response that an electro-optical system has to a point source
    The sharper the function, the sharper the object will appear in the system output image
    Difficult to directly measure
  Flight operations/installation
Values are determined in a laboratory and then validated in flight

## Slide 7: Common Spatial Resolution Metrics
Frequency Domain
Modulation Transfer Function (MTF)
  MTF at Nyquist typical parameter
Spatial Domain
Relative Edge Response (RER)
1.0
Cut-off frequency
Spatial frequency
MTF @ Nyquist
MTF
-2.0
-1.0
1.0
2.0
0
1.0
Ringing Overshoot
Ringing Undershoot
Region where mean slope is estimated
Edge Response
Pixels
0.0

## Slide 8: Modulation Transfer Function-MTF
MTF is a parameter described in the spatial frequency domain
  Mathematically allows you to model the imaging process by multiplication instead of convolution
  Not physically intuitive
  Evaluated in two separate orthogonal directions consistent with the along track and cross track of the image
MTF is defined as the magnitude of the OTF (Optical Transfer Function)
  OTF is defined as the Fourier Transform of the PSF

## Slide 9: General Image Quality Equation (GIQE)
Predicts NIIRS as a function of scale, imagery sharpness, contrast, SNR and image enhancement
Used to predict performance apriori
  Design of systems
  Insight on processing
  NIIRS = 10.251 – a log10 GSDGM + b log10 RERGM – 0.656 HGM – 0.344*G/SNR
  Where:
  GSDGM is the geometric mean of the ground sampled distance
  RERGM is the geometric mean of the normalized edge response
  HGM is the geometric mean-height overshoot caused by MTFC
  G is the noise gain associated with MTFC.
  If the RER >0.9, a=0.32 and b =0.559; otherwise, a=3.16 and b=2.817

## Slide 10: MTF and RER Relationships /Estimation
Measured edge response along “tilted edge”
Derivative of edge response or line spread function
Fourier transform of line spread function or MTF
Nyquist frequency is 0.5 * sampling frequency or (1/(2GSD))
-
5
-
4
-
3
-
2
-
1
0
1
2
3
4
5
0
0.5
1
Line Spread Funcation
FWHM
Distance / GSD
-15
-10
-5
0
5
10
15
500
1000
Distance / GSD
DN
Measured point
Best fit
0
0.5
1
0
0.5
1
Normalized spatial frequency
MTF
Nyquist frequency
MTF @
Nyquist frequency

## Slide 11: MTF@ Nyquist vs. RER (Gaussian PSF)
MTF and RER can be related to each other through Fourier analysis

## Slide 12: Effect of GSD on Image Quality
(Constant MTF = 0.7)
GSD = 1.5 in/4 cm
GSD = 6 in/15 cm
GSD = 2 ft/60 cm
GSD = 1 ft/30 cm

## Slide 13: Effect of MTF on Image Quality
MTF = 0.05
MTF = 0.4
MTF = 0.7
(Constant GSD = 16 cm/~6 in)

## Slide 14: Effect of MTF on Image Quality
MTF = 0.05
MTF = 0.4
MTF = 0.7
(Constant GSD = 30 cm/~12 in)

## Slide 15: Estimating MTF/RER Tilted Edge Technique
3 examples of undersampled edge responses measured across the tilted edge
Problem: Digital cameras undersample edge target
Solution: Image tilted edge to improve sampling
Superposition of 24 edge responses shifted to compensate for the tilt
 – edge tilt angle
 – pixel index
x – pixel’s distance from edge (in GSD)
Pixels
Distance/GSD
DN
DN

## Slide 16: Traditional Engineered Spatial Resolution Targets
Fort Huachuka
tri-bar target
Deployable targets at South Dakota State University
Causeway bridge over Lake Pontchartrain
Digital Globe provided satellite imagery
Pong Hu, Taiwan
These types of targets however, will not generally be available in the imagery to validate spatial resolution
Finnish Geodetic Institute Sjökulla Site

## Slide 17: Problem…
Most commonly used spatial resolution estimation techniques require engineered targets (deployed or fixed), which are not always available or convenient
Target size scales with GSD
  Edge targets are typically uniform edges 10-20 pixels long and ~10 pixels tilted a few degrees relative to pixel grid (improve sampling)
  Increasing GSD increases difficulty
    Moderate resolution systems such as Landsat use pulse targets

## Slide 18: Spatial Resolution Estimation Using In-Scene Edges
Exploit edge features in nominal imagery
  Edge response estimation is performed without dedicated engineered targets
Appropriate for high spatial resolution Imagery
Automated processes exist that can
  Identify edges and screen them
  Construct resulting edge response
  Calculate MTF and RER
Building Shadows
Rooflines

## Slide 19: MTF/RER with Natural Edges

## Slide 20: Effect of SNR on Image Quality
IKONOS Imagery
SNR ~ 100
IKONOS Imagery
with noise added
SNR ~ 2
Includes material © Space Imaging LLC

## Slide 21: Radiometry

## Slide 22: Relative Radiometry
Digital Number (DN) functional relationship with brightness (radiance), aperture and integration time (Linearity/Dynamic Range)
Quantization (Typical for Aerial Data Spec)
Pixel-to-pixel (image normalization or flat fielding)
Band-to-band (spectrum) (Colorimetry)
Typical remote sensing industry goal <1%

## Slide 23: Absolute Radiometry /Colorimetry
Absolute Radiometry
  Conversion of DN to engineering units of radiance (remote sensing)
  Typical remote sensing goal is <5% difference from a National Standard (Landsat Data Continuity Mission (LDCM) Data Specification, March 2000)
Colorimetry
  Ability to produce true colors from sensor intrinsic RGB
In general if a system has good relative radiometry then good color balancing can be achieved. Similarly systems that have good absolute radiometry have good color balance

## Slide 24: Absolute Radiometric Calibration
Using the spectral response and integrating sphere radiance both
normalization and absolute calibration can be accomplished simultaneously
Calibration Integration Time
Calibration F#
Maximum Reference DN
Integrating Sphere In-band Radiance

## Slide 25: Why Have An Absolute Radiometry Imaging System?
Predicts the performance of the multispectral imager a priori
For aerial systems simulates satellite performance
Supports the ability to atmospherically correct products to surface reflectance
  Change detection and time series analysis

## Slide 26: Calibration/Validation Model of Operation
Baseline sensor performance in a controlled environment
Cal/Val critical sensors
Laboratory-based Verification & Validation
Instrument Calibrations
In-Flight Verification & Validation
Cal/Val installed sensors
Cross-validate systems
Temporal degradations
Provide NIST-traceable standards
Cal/Val foundation

## Slide 27: Camera Radiometric Characterization
Radiometric calibration and linearity measured with integrating sphere source
-2
0
2
4
6
8
10
0
50
100
150
200
250
300
Radiance
DN
-2
0
2
4
6
8
10
12
14
16
0
50
100
150
200
250
300
Radiance
DN
-5
0
5
10
15
20
25
30
35
40
0
50
100
150
200
250
300
Radiance
DN
-5
0
5
10
15
20
25
30
35
0
50
100
150
200
250
300
Radiance
DN
Linearity
Measurements
Characterization of Radiance Sources
Radiance Setup
Integrating Sphere
CCD Camera

## Slide 28: Camera Spectral Response
Monochromatic Uniform Source
Multispectral CCD Camera Response

## Slide 29: Sample Integrating Sphere Raw Image and Corresponding Histogram
29
Signal changes by more than a factor of 2
560 nm Wavelength

## Slide 30
Vignetting Image of Integrating Sphere

## Slide 31: Before and After (430.1 nm)

## Slide 32: Integrating Sphere Image

## Slide 33: Corrected Integrating Sphere Image

## Slide 34: Corrected vs Uncorrected (Water)

## Slide 35: In-Flight Absolute Radiometric Accuracy
Requires knowledge of
  System spectral response Illumination as a function of wavelength and viewing geometry
  Target properties (reflectance)
  Atmosphere (in-flight assessments)
Outcome is a calibration coefficient
  Shown as a slope
DN
Radiance

## Slide 36: Summary
In addition to geopositional accuracy, image quality is determined by:
  Spatial resolution
  Radiometric accuracy
Typical measures of merit are:
  Spatial resolution – GSD, MTF at Nyquist and RER, SNR
  Radiometric accuracy - Calibration coefficient
Each of these must be determined in the laboratory prior to operation and then validated in-field
Required values are highly dependant on application

## Slide 37: Backup

## Slide 38: Data Product Specification Terms Recommendation
Spatial Resolution
  GSD
  RERx, RERy (across the sensor) or MTF@Nyquist
Spectral
  Spectral response (Center Wavelength, FWHM)
Radiometry
  Quantization
  SNR at different radiances or part of dynamic range
  Relative (Linearity, pixel-to-pixel, band-to-band)
  Absolute (Only for science projects)

## Slide 39: Data Product Specification Terms Recommendation
Gepositional
  CE90, LE90

## Slide 40: Summary
Both the aerial and satellite MS remote sensing communities would benefit from common terms
Interoperability will require much more extensively characterized systems
  Surface reflectance is highly desired for environmental studies
Automated in-field techniques needed

## Slide 41: Electro-Optical Image Quality
Sensor calibration and data product validation is more than just metric calibration…
Spatial Resolution
  A measure of the smallest feature that can be resolved or identified within an image
Radiometric Accuracy
  A measure of how well an image DN can be related to a physical engineering unit
  Engineering units are required to perform atmospheric correction to pull out surface reflectance or temperature values from within a scene.

## Slide 42: Relative Edge Response-RER
Another measure of spatial resolution is a difference of normalized edge response values at points distanced from the edge by -0.5 and 0.5 GSD
Relative Edge Response is one of the engineering parameters used in the General Image Quality Equation to provide predictions of imaging system performance expressed in terms of the National Imagery Interpretability Rating Scale
-2.0
-1.0
1.0
2.0
0
1.0
Ringing Overshoot
Ringing Undershoot
Region where mean slope is estimated
Edge Response
Pixels
0.0

## Slide 43: Meaning of RER in Remote Sensing
Radiance measured for each pixel is assumed to come from the Earth’s surface area represented by that pixel. However, because of many factors, actual measurements integrate radiance L from the entire surface with a weighting function provided by a system’s point spread function (PSF):
Part of radiance that originates in the pixel area is given by:
Relative Edge Response squared (RER2) can be used to assess the percentage of the measured pixel radiance that actually originates from the Earth’s surface area represented by the pixel:
GSD
A simple example:
Box PSF
Width = 2 GSD
ER(0.5) - ER(-0.5) =
0.75 - 0.25 = 0.50
RER = 0.50
RER2 = 0.25 means that 25% of information collected with the pixel PSF (blue square) comes from the actual pixel area (shadowed square)
Source: Blonski, S., 2005. Spatial resolution characterization for QuickBird image products: 2003-2004 season. In Proceedings of the 2004 High Spatial Resolution Commercial Imagery Workshop, USGS, Reston, VA, Nov 8–10, 2004

## Slide 44: Radiometric Accuracy
Absolute radiometric calibration
  DN values are related physical units on an absolute scale using national standards
Relative radiometric calibration
  DN values are related to each other
    Image-to-image
    Pixel-to-pixel within a single image
Determined in a laboratory prior to sensor operation and validated in flight

## Slide 45: Why Have An Absolute Radiometrically Calibrated Aerial Imaging System?
Predicts the performance of the multispectral imager a priori
Simulates satellite remote sensing systems
Supports the ability to atmospherically correct products to surface reflectance
Improves quality control in manufacturing process by measuring camera sensitivities during laboratory calibration
Reduces need to color balance with post processing software

## Slide 46: Absolute Calibration Accuracy
Absolute radiometric calibration accuracy depends on knowledge of measurements
  Using current methods, accuracy can only be validated to within 2-5%
  In-field calibration accuracy also depends on knowledge of solar irradiance models
Required accuracy depends on application

## Slide 47: Absolute Radiometric Calibration Coefficient
Where: DN | Digital Number for a pixel
L | Spectral radiance of Integrating sphere [W/(m2 sr mm)]
S | System spectral response
C | Calibration coefficient [(W/(m2 sr mm))/DN]

## Slide 48: Absolute Radiometry Enables Atmospheric Correction
Atmospherically corrected imagery (reflectance maps) enable:
  Change detection with reduced influence of atmosphere and solar illumination variations
  Spectral library-based classifiers
  Improved comparisons between different instruments and acquisitions
  Derived products such as Normalized Difference Vegetation Index (NDVI)

## Slide 49: Importance of Atmospheric Correction
Wavelength, microns
Radiance, Wm-2sr-1microns-1

## Slide 50: Relative Radiometric Accuracy
Laboratory measurements are performed using uniform illuminated targets
  Flat fielding
    Focal plane roll-off is measured and corrected for so that each pixel yields the same DN across the focal plane
  Focal plane artifact removal
    Artifacts such as focal plane seams and bad pixels are removed and replaced with either adjacent pixel values or an average of adjacent pixel values
Typical remote sensing goal is <1%

## Slide 51: Sample Flat Fielding Correction

## Slide 52: Flat Fielding
Flat Fielded Dark Frame Subtracted Image
Normalized to Reference Condition DN
Raw DN
Mean Dark Image
Integrating Sphere Bright Image at Reference F#
Maximum DN